夹支扁球壳自由振动问题的准Green函数方法

李善倾，袁 鸿，刘人怀

（暨南大学 力学与土木工程系，广东 广州 510632）

摘要：将准Green函数方法应用于求解夹支任意形状底扁球壳的自由振动问题。即利用问题的基本解和边界方程构造一个准Green函数，这个函数满足了问题的齐次边界条件。采用Green公式将夹支任意形状底扁球壳自由振动问题的振型控制微分方程化为第二类Fredholm积分方程。通过边界方程的适当选择，积分方程核的奇异性被克服了。最后通过离散化方程求得数值结果.数值算例表明，该方法具有较高的精度，计算量小，收敛速度快，是一种新型有效的数学方法。

关键词：Green函数；积分方程；R-函数；夹支扁球壳；自由振动

中图分类号：       文献标识码：    文章编号:

引言

扁球壳是指其最大矢高和底面直径之比一般应小于1/5。扁球壳在土木、水利、机械、船舶、航空航天等工程中都有着广泛的应用。扁球壳作为工程结构的主要部件，在进一步的设计与研究中需考虑其动力问题，而自由振动作为扁球壳动力问题的基础应首先予以分析。 扁球壳的自由振动问题，最重要的是求固有频率，尤其是最低阶固有频率。力学工作者对小挠度扁球壳振动问题已经做了大量的研究工作，并取得了许多研究成果。本文应用准Green函数方法分析夹支任意形状底扁球壳的自由振动问题.Green函数方法广泛用来解决各种边值问题，然而，对于二维或高维问题，建立Green函数是极其复杂的，只有在极其简单的区域上（如圆、球），可以找到Green函数,困难在于虽然易于找到满足基本方程的函数（基本解），却难以满足问题的齐次边界条件.如果以基本解代替Green函数，将得到边界积分方程，它一般是一个在边界上具有奇异性的积分方程。针对边界积分方程存在的问题，准Green函数方法采用了另一条途径推导积分方程。应用准Green函数、边界方程及Green公式可将双调和算子方程化为积分方程。用有限元法或有限差分法求解板壳问题时，需对整个研究区域划分单元网格，前处理工作量大，数据准备麻烦，花费大量机时。边界元法则克服了区域型数值方法的缺点，只在边界上划分单元，通过基本解把域内未知量化为边界未知量来求解，使自由度数目大大减少，但这种方法却存在大量奇异积分，而且在边界及其附近区域上解的精度较低。

本文应用Rvachev[1]提出的R-函数理论和准Green函数方法，分析了夹支任意形状底扁球壳的自由振动问题。利用问题的基本解构造一个准Green函数。这个函数满足了问题的齐次边界条件，但没能满足基本微分方程.而建立准Green函数的关键在于将问题的边界用规范化方程表示出来，问题的区域由不等式表示出来。将存在多种选择，经过适当的数学处理，积分方程核的奇异性可以被克服。R-函数理论保证了对于任何复杂的区域，总可以找到函数，从而可将原问题化为无奇异性的第二类Fredholm积分方程。使用这一方法，袁鸿等已成功求解了简支及固支各向同性薄板、简支扁球壳自由振动及弯曲问题[2-7]。准Green函数方法是一种新颖的数学思想，是一种值得研究的新数值方法。与有限元法或有限差分法相比，准Green函数方法在解决的板壳问题方面，对整个研究区域划分单元网格很少，前处理工作量相对小很多，收敛速度快，计算量小，可求得很高精度的结果。本文将准Green函数方法应用于求解夹支任意形状底扁球壳的振动问题。通过夹支矩形底、梯形底扁球壳的数值结果证明了本文方法的有效性和可行性。

1基本方程

扁球壳的自由振动微分方程组为：

，      (1)

，(2)

式中，为应力函数，为壳体的径向挠度，为曲率半径，，为笛卡儿坐标系中扁球壳的底面(平面)所包含的域，为双调和算子，弯曲刚度，是壳的厚度，和分别是弹性模量和泊松比，为单位面积内的质量，是时间变量。

滑动夹支边界条件为：

(3)

式中，是拉普拉斯算子，表示的边界，为边界曲线的外法线方向。

由式(1)和(3)式，可得

(4)

把表达式(4)代入(2)式，可得所单独满足的微分方程为

(5)

设

(6)

式中，和为常系数，为固有频率, 表示振型函数。

将表达式(6)代入(5)式可得夹支扁球壳的振型控制微分方程及边界条件为

,(7)

， ,        (8)

2 积分方程的推导

设是边界的一阶规范化方程，即满足[8]：

，,       (9)

,          (10)

构造准Green函数如下

(11)

(12)

其中

(13)

(14)

(15)

其中，、分别表示、方向的单位向量，，。

显然准Green函数满足条件

(16)

(17)

为了将边值问题(7)和(8)化为积分方程，应用函数类的Green公式，对所有的、有

(18)

用式(8)中的和式(11)中的分别代替式(18)中的、，并注意到是双调和算子的基本解[8]，利用式(7)、(8)、(16)和 (17)可得

(19)

式中

(20)

将表达式(12)代入式(20)中，进行推导，可

以得到 的具体表达式。

(21)

式中，，。

当时，即且时，表达式(21)中才可能出现不连续性.实际上，当时，式(21)为

(22)

为了使积分核，将式(22)的分子展开成的幂级数后，幂级数的常数项和1次项的系数必须等于0。 下面通过构造一个新的边界规范化方程来保证的连续性，为此假设

(23)

式中，是边界的一阶规范化方程，即满足式(9)和式(10)。显然，也是一阶规范化方程。容易证明。 只要选取

(24)

就能保证在积分域内处处连续，将表达式(24)代入式(23)中，可得

(25)

因此，我们可以通过任意选择一个边界规范化方程，就可以根据式(25)建立一个新的边界规范化方程，从而就可以保证积分核的连续性。

3 积分方程的离散

夹支扁球壳自由振动问题的等效积分方程(19)进行离散化。将积分域划分为若干子域，在各子域中分别应用中矩形公式进行数值求积。则积分方程(19)可化为齐次线性代数方程组：

， (26)

其中是划分的子域数， 是在处的未知虚拟值。

，

当时, ,

当时,,

,

表示第个子域的面积。

齐次线性方程组(26)有非平凡解的条件是其系数行列式等于零，即：

(27)

求解式(27)，可以得到前阶固有频率，或.将求得的各阶固有频率代入线性方程(26)中，还可以求出各子域上挠度的比值，即各阶振动的模态。

4 数值算例

例1图1所示夹支扁球壳，当0.75，=2时为矩形底扁球壳，扁球壳半径，最大矢高，取壳厚度=0.1，泊松比，弹性模量取=，单位面积内的质量取=780.根据R-函数理论[8 ]，只要取：

，

式中，

,

则是矩形底边界的一阶规范化方程，

，分别表示夹支矩形底扁球壳的各个边。本文方法只用1111矩形子域划分形式如图2所示，研究了半径取不同值时的夹支矩形底扁球壳的固有频率计算结果列于表1中，其计算结果就与ANSYS有限元法(FEM)采用200200矩形网格划分时的计算结果吻合得很好。

表1  夹支矩形底扁球壳不同半径R值的固有频率f

Tab.1 Natural frequency f of slip clamped rectangular shallow spherical shell with different R

|  | 模态阶数 |
| --- | --- |
|  | 1 |  | 2 |  | 3 |  | 4 |  | 5 |
|  | 本文方法 | 有限元法 | 本文方法 | 有限元法 | 本文方法 | 有限元法 | 本文方法 | 有限元法 | 本文方法 | 有限元法 |
| 3 | 51.212 | 50.338 | 72.028 | 71.896 | 96.230 | 95.494 | 112.90 | 111.41 | 120.63 | 118.15 |
| 4 | 46.359 | 45.391 | 68.663 | 68.524 | 93.738 | 92.982 | 110.78 | 109.27 | 118.65 | 116.13 |
| 5 | 43.932 | 42.909 | 67.047 | 66.905 | 92.561 | 91.795 | 109.79 | 108.26 | 117.72 | 115.18 |
| 6 | 42.555 | 41.498 | 66.154 | 66.009 | 91.915 | 91.144 | 109.24 | 107.71 | 117.21 | 114.66 |
| 7 | 41.703 | 40.624 | 65.609 | 65.463 | 91.524 | 90.750 | 108.91 | 107.37 | 116.91 | 114.35 |

例2  图1所示夹支梯形底扁球壳，1.2，1.0，1.1，扁球壳半径3，最大矢高0.273，取壳厚度=0.1，泊松比，弹性模量取=，单位面积内的质量取=780。根据R-函数理论[8]，只要取：

，

式中， ，

，    ，

则是梯形底边界的一阶规范化方程，，，分别表示夹支梯形底扁球壳的各个边。研究了半径取不同值时的夹支梯形底扁球壳的固有频率，计算结果列于表2中，并与ANSYS有限元法的计算结果进行了对比。采用图3的梯形子域划分形式，本文方法只用1111子域的结果就与ANSYS有限元法用200200梯形网格的结果吻合得相当好。从表1-2的比较结果，可知准Green函数方法采用子域数远少于ANSYS有限元法，理论计算量小了很多，收敛速度快，精度比较好，这正是本文方法的优越性和正确性。

表2   夹支梯形底扁球壳不同半径R值的固有频率f

Tab.2 Natural frequency f of slip clamped trapezoidal shallow spherical shell with different R

|  | 模态阶数 |
| --- | --- |
|  | 1 |  | 2 |  | 3 |  | 4 |  | 5 |
|  | 本文方法 | 有限元法 | 本文方法 | 有限元法 | 本文方法 | 有限元法 | 本文方法 | 有限元法 | 本文方法 | 有限元法 |
| 3 | 69.242 | 69.086 | 85.020 | 85.487 | 114.95 | 115.92 | 159.89 | 160.13 | 162.21 | 161.41 |
| 4 | 65.734 | 65.572 | 82.189 | 82.674 | 112.87 | 113.86 | 158.40 | 158.64 | 160.75 | 159.94 |
| 5 | 64.046 | 63.880 | 80.844 | 81.339 | 111.89 | 112.89 | 157.71 | 157.95 | 160.06 | 159.25 |
| 6 | 63.109 | 62.942 | 80.104 | 80.604 | 111.36 | 112.37 | 157.33 | 157.57 | 159.69 | 158.88 |
| 7 | 62.537 | 62.370 | 79.655 | 80.158 | 111.04 | 112.05 | 157.10 | 157.35 | 159.47 | 158.65 |

5 结  论

本文应用R-函数理论和准Green函数方法，研究了夹支任意形状底扁球壳的自由振动问题。通过将本文方法的计算结果跟ANSYS有限元法的结果进行比较，计算量小，收敛速度快，有其优越性，表明本文方法是可行有效的、合理的。其为研究复杂边界形状扁球壳问题提供了一种新型有效的计算手段。准Green函数方法是一种新的数值方法，提高其计算精度及开拓其应用领域，有待进一步研究。R-函数理论还可用来构造满足边界条件的试函数，与Ritz法、变分法和样条函数近似法等[9-15]数值方法结合起来，有效地解决各种具有复杂边界形状的板壳力学问题。

参考文献：

RVACHEV V L. Theory of R-function and Some of its Application[M]. Kiev: Nauk Dumka,1982:415-421.( in Russian)

袁鸿, 李善倾, 刘人怀．Pasternak地基上简支板振动问题的准格林函数方法[J]．应用数学和力学, 2007, 28(7): 757-762.

YUAN Hong, LI Shanqing, LIU Renhuai. Green quasifunction method for vibration of simply-supported thin polygonic plates on Pasternak foundation[J]. Applied Mathematics and Mechanics(English Edtion), 2007, 28(7):847-853.

李善倾,袁鸿. 简支梯形底扁球壳自由振动问题的准Green函数方法[J]. 应用数学和力学,2010,31(5):602-608.

LI Shanqing, YUAN Hong. Quasi-Green’s function method for free vibration of simply-supported trapezoidal shallow spherical shell [J]. Applied Mathematics and Mechanics (English Edtion), 2010, 31(5), 635-642.

Shanqing Li, Hong Yuan. Green quasifunction method for free vibration of simply-supported trapezoidal shallow spherical shell on Winkler foundation[J]. Acta Mechanica Solida Sinica, 2010,23 (4):370-376.

李善倾,袁鸿. Winkler地基上固支薄板自由振动问题的准Green函数方法[J]. 应用数学和力学,2011,32(3):253-262.

LI Shanqing, YUAN Hong. Quasi-Green’s function method for free vibration of clamped thin plates on Winkler foundation [J]. Applied Mathematics and Mechanics (English Edtion), 2011, 32(3), 265-276.

李善倾, 袁鸿, 薛兴伟. 简支梯形底扁球壳弯曲问题的准格林函数方法[J]. 计算力学学报, 2011,28(2):270-273.

LI Shanqing, YUAN Hong, XUE Xingwei. Green quasifunction method for bending problem of simply-supported trapezoidal shallow spherical shells[J]. Chinese Journal Computational Mechanics, 2011, 28(2): 270-273. (in Chinese)

Shanqing Li, Hong Yuan. Green quasifunction method for free vibration of clamped thin plates [J]. Acta Mechanica Solida Sinica, 2012, 25(1): 37-45.

Ortner V N. Regularisierte faltung von distributionen. Teil 2: Eine tabelle von funda- mentallocunngen[J]. ZAMP, 1980, 31(1): 155-173.

Kurpa L V, Reached V L and Ventsel E. The R-function method for the free vibration analysis of thin orthotropic plates of arbitrary shape[J]. Journal of Sound and Vibration, 2003,261(1):109-122.

Kurpa L V, Lyubitska K I and Shmatko A V. Solution of vibration problems for shallow shells of arbitrary form by the R-function method[J]. Journal of Sound and Vibration, 2005, 279:1071-1084.

Kurpa L V, Pilgun G and Amabili M. Nonlinear vibrations of shallow shells with complex boundary: R-functions method and experiments[J]. Journal of Sound and Vibration, 2007,306:580-600.

Kurpa L V, Shmatko T and Timchenko G. Free vibration analysis of laminated shallow shells with complex shape using the R- functions method[J]. Composite Structures, 2010, 93(1):225-233.

Breslavsky I D and Avramov K V. Nonlinear modes of cylindrical panels with complex boundaries : R-function method [J]. Meccanica, 2011,46(4): 817-832.

Awrejcewicz J, Kurpa L and Osetrov A. Investigation of the stress-strain state of the laminated shallow shells by R-functions method combined with spline-approximation[J]. ZAMM, 2011, 91(6): 458-467.

Pilgun G and Amabili M. Non-linear vibrations of shallow circular cylindrical panels with complex geometry: Meshless discretization with the R-functions method [J]. International Journal of Non-Linear Mechanics, 2012, 47: 137-152.

Quasi-Green’s function method for free vibration of slip clamped shallow spherical shell

LI Shan-qing, YUAN Hong

(MOE Key Laboratory of Disaster Forecast and Control in Engineering, Institute of Applied Mechanics, Department of Mechanics and Civil Engineering, Jinan University, Guangzhou 510632, P. R. China)

Abstract: The quasi-Green’s function method is employed to solve the free vibration of slip clamped shallow spherical shell with arbitrary boundary shape. A Green quasi-function is established by using the fundamental solution and boundary equation of the problem. This function satisfies the homogeneous boundary condition of the problem. The mode shape differential equation of the free vibration problem of slip clamped shallow spherical shell with arbitrary boundary shape is reduced to Fredholm integral equation of the second kind by Green’s formula. Irregularity of the kernel of integral equation is overcome by choosing a suitable form of the normalized boundary equation. Finally, the numerical results can be obtained from the discretization equations. Numerical examples demonstrate that the method has high precision, small amount of calculation, and fast convergence rate, and it is a new kind of effective mathematical methods.

Key words: Green function; integral equation; R-function; clamped shallow spherical shell; free vibration

作者简介：李善倾(1982—),男,讲师。电话:15975638598, E-mail: lishanqing09@163.com

袁  鸿(1963—),男,教授。电话:13660265906, E-mail: tyuanhong@jnu.edu.cn

# Text boxes

图1  夹支扁球壳

Fig.1 Slip clamped shallow spherical shell

0

(b, c)

(-d, c)

(-e, 0)

O

图2矩形积分域划分

Fig.2 Division of rectangular integral domain

O

图3梯形积分域划分

Fig.3 Division of trapezoidal integral domain